RaveModemFactory
Software architecture
Aleksander Morgado
 <aleksander@aleksander.es>

ChangeLog
Date	Version	Changes
2020-07-12	8	Update for RaveModemFactory 1.30: / Updated section 1 Introduction to list EM7565 as supported devices. Also updated libqmi and GLib version requirements. / New section 3.5 Dual SIM support. / Updated section 3.8 Network disconnection adding details about when implicit disconnections may happen. / New section 4.3.6 Dual SIM management API with the new methods to allow SIM slot selection. / Updated section 5 rmfcli to include the new SIM slot selection operations.
2017-01-18	7	Update for RaveModemFactory 1.28: / Updated section 1 Introduction to list MC74xx as supported devices. / Updated section 3.3 Device initialization with details about how the link layer protocol is selected. / Updated section 3.4 SIM management with notes about now using the UIM service instead of DMS UIM commands.
2016-07-01	6	Minor update: / Updated section 5 rmfcli to specify that rmfcli is just a test tool.
2016-06-29	5	Update for RaveModemFactory 1.26: / Updated sections 1.2 Components and 3.1 Startup with information about how the TCP/IP based support works. / Added section 4.3.1, Library initialization API to specify how to select between local or TCP/IP based operations.
2015-04-02	4	Update for RaveModemFactory 1.24: / Updated section 4.3.10 Network connection API with the new GetDataPort() method. / Updated section 5 rmfcli with the new --get-data-port action.
2015-04-01	3	Update for RaveModemFactory 1.22: / Updated section 4.3.7 Power management API with the new PowerCycle() method. / Updated section 5 rmfcli with the new --power-cycle action.
2015-03-19	2	Update for RaveModemFactory 1.20: / Added section 3.10 Statistics.
2015-02-20	1	Initial version.

# Introduction
The RaveModemFactory is a connection manager that allows to use 3GPP mobile broadband modems (e.g. GSM, HSPA, or LTE) implementing the Qualcomm MSM Interface (QMI) protocol. This protocol will be available in modems with Qualcomm Gobi 3G/4G chipsets, like e.g.:
- Sierra Wireless 9200 family (MC7700, MC7710…)
- Sierra Wireless 9x15 family (MC7304, MC7330, MC7354…)
- Sierra Wireless 9x30 family (MC7430, MC7455...)
- Sierra Wireless 9x50 family (EM7565, EM7511...)
3GPP2 technologies (e.g. CDMA or EV-DO) are not currently supported.
The RaveModemFactory system provides a simple and stateless interface to the basic operations that can be performed with a mobile broadband modem.
One of the major advantages of the system is that the user does not need to know which kind of modem is connected to the system, or which interfaces are exposed, or how to control those interfaces. The RaveModemFactory will work with every QMI-capable modem, regardless of manufacturer or version.
The user application will just need to use the RaveModemFactory interfaces to fully interact with the modem, as well as to get a fully established Internet connection.
## Dependencies
Illustration 1: High level architecture
The RaveModemFactory software is based on several system level tools, including:
- Linux kernel with the cdc-wdm (since Linux 2.6.26) and qmi_wwan[1] (since Linux 3.4) drivers. Support for the Sierra Wireless 9x30 family (MC74xx devices) and 9x50 family (EM75xx devices) only since Linux 4.5.
  [1] https://sigquit.wordpress.com/2014/06/11/qmiwwan-or-gobinet/
- The Glib/GIO[2] (>= 2.48) libraries. These libraries are the core foundation libraries of the GNOME project, and provide a general-purpose set of tools for C-based applications.
  [2] https://developer.gnome.org/gio/stable/
- The GUdev[3] (>= 147) library. This library provides a Glib/GIO based interface to use the udev[4] device manager (e.g. for automatic device discovery).
  [3] http://www.freedesktop.org/software/systemd/gudev/
  [4] http://en.wikipedia.org/wiki/Udev
- The libqmi[5] (>= 1.26) library. This library exposes a simple Glib/GIO based asynchronous interface to use the QMI protocol with the modem. Along with the library, a qmicli tool will also be available, which allows to use the QMI protocol directly from command line.
  [5] https://sigquit.wordpress.com/2012/08/20/an-introduction-to-libqmi/
- The iproute2[6] tools to manage network interfaces.
  [6] http://en.wikipedia.org/wiki/Iproute2
- The ISC dhclient[7] DHCP client daemon.
  [7] https://www.isc.org/downloads/dhcp/
## Components
The RaveModemFactory system is itself built as 3 different components:
- The rmfd system daemon, developed in C using the Glib/GIO library, which takes care of the actual control of the modem (including network interface and routing rules setup).
- The librmf library, developed in C++, which provides a simple interface for the actions available through the rmfd daemon. The communication between the rmfd daemon and the librmf library is done either through a standard Unix socket[8] or through a TCP/IP socket.
  [8] The unix socket is by default exposed at /tmp/rmfd-server.
- The rmfcli tool, developed in C++, which provides a command line interface for all the operations exposed by the librmf shared library.
Although the command line interface is a fully functional tool, applications wanting to use the RaveModemFactory are expected to link to the shared librmf library.

# Architecture
The following diagram depicts a typical setup of the RaveModemFactory components and how they interact with the other system tools. The user application in the diagram will use the shared librmf library interfaces to control the modem and gather status information from it.
The blocks in the diagram are organized by color as follows:
Illustration 2: Low-level architecture
- Dark red: the RaveModemFactory components.
- Light red: other userspace programs and libraries.
- Orange: the modem interfaces exposed by the kernel.
- Blue: the kernel and its drivers.
- Green: the modem hardware.
# Basic operation
## Startup
The rmfd daemon is setup as a system daemon that should be automatically launched as any other service in the system (e.g. via init scripts or systemd service units). In the same way, the daemon should be shutdown when the system is going to be halted.
If no additional option is given when launching the rmfd daemon, it will listen by default in the local UNIX socket. For the TCP/IP based operation the daemon expects these additional options:
Usage: rmfd <option>

Application Options:
  -y, --address=[IP] IP address where to enable the TCP listener
  -Y, --port=[PORT] Port where to enable the TCP listener

## Device discovery
The kernel is in charge of detecting the Qualcomm Gobi modem via its USB 2.0 subsystem. Once the USB device is detected and configured, the qmi-wwan and cdc-wdm kernel drivers will take care of the QMI interfaces. For every QMI-capable USB interface, the qmi-wwan driver will expose a wwan network interface, and the cdc-wdm driver will expose an associated /dev/cdc-wdm character device.
Once the network and character devices are exposed by the kernel, they will also get notified via the udev device manager. The rmfd daemon listens to udev events, and will therefore automatically discover that a QMI modem is available.
## Device initialization
Before using the mobile broadband modem, the rmfd daemon needs to fully initialize the device. Among other things, the following steps will be performed:
- The daemon will make sure that a specific /dev/cdc-wdm character device will be used to get a specific wwan network connected.
- The QMI protocol will be reset so that any previously allocated service clients are disposed.
- Link layer protocol [9] [10]:
  [9] The default USB configuration in the Sierra Wireless MC73xx modems will expose 2 pairs of wwan interfaces, one configured by default to use 802.3 data format, and the other one raw IP packets.
  [10] The Sierra Wireless MC74xx modems only support raw IP packets.
  - On kernels before 4.5, the network interface will be explicitly configured to use 802.3 data format as well as no QoS headers.
  - On kernel 4.5 or newer, the network interface will be configured to use the same data format as reported by the modem, either 802.3 or raw IP.
- The QMI protocol version information of the device will be preloaded in the QMI stack.
- The daemon will initialize several service-specific QMI clients, for the DMS (device management), NAS (network access), UIM (user identity module) and WMS (wireless messaging) services.

## SIM management
The RaveModemFactory system allows performing different SIM management[11] operations, including SIM-PIN unlocking, enabling/disabling or changing.
[11] Since RaveModemFactory v1.28.0, the SIM management commands are based on the complex "UIM" QMI service, instead of the simpler "DMS" QMI service specific "DMS UIM" commands, as these were obsoleted in the new Sierra Wireless MC74xx devices.
The application using the RaveModemFactory system will need to make sure that the SIM-PIN is unlocked before trying to use the modem. The librmf library provides methods to both check if the unlock is necessary, and also to actually send the unlock code to the modem.
The SIM-PIN unlock operation will by default make sure that the SIM is fully initialized before returning the action result to the caller.
## Dual SIM support
Since RaveModemFactory 1.30, the system allows controlling two separate SIMs, but with only one active at any given time.
The user may switch between both SIMs, and upon each switch operation the modem will unregister from the network and re-register with the new SIM details. If the modem is connected while a SIM switch happens, it will also be automatically disconnected.
The librmf library provides methods to check which is the current active SIM slot, and to switch between the two supported slots.
## Network registration
Once SIM-PIN has been successfully unlocked or if SIM-PIN lock was already disabled (in the currently active SIM card), the rmfd daemon will automatically request the modem to register in the home network. If the home network is not available, the modem will try to register in any roaming network where it's allowed to register. If the automatic registration procedure doesn't get the modem registered in 60s, the daemon will launch an explicit network scan operation to list the available networks, and once the scan is finished, it will restart the automatic registration in the home network.
## Network connection
Once the modem is registered in a network, the user of the RaveModemFactory system will be able to request the modem to get connected to a specific APN. If the APN requires authentication, additional username and password parameters can also be given during the connection procedure.
If the connection call doesn't fail, the modem will be reported as connected in the QMI stack. The rmfd daemon will then bring the associated wwan interface up (using either ifconfig or iproute2) and will also request the IP, routing and name resolution setup via DHCP (using dhclient). The built-in DHCP server in the modem will take care of providing the expected settings to use.
Given that even the DNS resolution configuration is being managed, the rmfd daemon will backup the previous configuration[12] and will restore it whenever the QMI wwan interface gets disconnected.
[12] /etc/resolv.conf
Routing-wise, the rmfd daemon will take care of the default route once the QMI wwan interface gets connected, but will not re-select any other default route when disconnected.
## Network disconnection
Network disconnection can be explicitly requested by the users of the RaveModemFactory system, or automatically happening due to other conditions (e.g. the network may request the disconnection, or the disconnection may be implicitly happening as part of a SIM switch operation).
When disconnected, the wwan network interface will be brought down, the DNS resolution configuration will be restored, and the call will be stopped in the QMI stack.
## SMS messaging
The rmfd daemon will by default log to syslog all the SMS messages received by the mobile broadband modem, e.g.:
jan 12 11:27:03 athena rmfd[12805]: SMS [Timestamp: 150112112700+01] [From: +34639335936] This is the SMS text content
The Timestamp: field gives the SMS timestamp (YYMMDDhhmmss+utc offset), and the From: field indicates the sender number.
## Statistics
The rmfd daemon keeps track of the ongoing connection statistics, as well as the monthly accumulated ones.
Each ongoing session is tracked in a stats log file[13], with a new record written every 10s containing the modem-reported statistics and other state values. Each record contains a list of TAB-separated fields, including:
[13] /var/log/rmfd.stats
- Type of record: S (start), P (partial) or F (final). When connection is launched, a S record is written, then P records every 10s until a last F record when disconnected in a controlled way.
- Start timestamp: Date and Time of when the connection was started. If the time can be retrieved from the modem itself it will be given in ISO8601 format, and otherwise it will include the Unix timestamp of the system.
- Record timestamp: Date and Time of when the record was written. If the time can be retrieved from the modem itself it will be given in ISO8601 format, and otherwise it will include the Unix timestamp of the system.
- Duration: Duration of the ongoing session, given in seconds.
- Bytes RX: Total bytes received, as measured by the modem itself.
- Bytes TX: Total bytes transmitted as measured by the modem itself.
- Radio interface: Radio interface being used in the connection (e.g. gsm, umts or lte).
- RSSI: Received Signal Strength Indication, given in dBm.
- MCC: Mobile country code of the serving system.
- MNC: Mobile network code of the serving system.
- LAC: Location area code of the serving system.
- CID: Cell ID of the serving system.
An full example of a single connection session would look like the following:
S	2015-03-19 09:49:56	2015-03-19 09:49:56	0	0	0	umts	-95	214	3	1140	10774738
P	2015-03-19 09:49:56	2015-03-19 09:50:06	10	22591	13816	umts	-95	214	3	1140	10774738
P	2015-03-19 09:49:56	2015-03-19 09:50:16	20	22845	14183	umts	-95	214	3	1140	10774738
P	2015-03-19 09:49:56	2015-03-19 09:50:26	30	22845	14183	umts	-95	214	3	1140	10774738
P	2015-03-19 09:49:56	2015-03-19 09:50:36	40	22845	14426	umts	-95	214	3	1140	10774738
P	2015-03-19 09:49:56	2015-03-19 09:50:46	50	23565	14502	umts	-104	214	3	1140	10774738
P	2015-03-19 09:49:56	2015-03-19 09:50:56	60	23565	14502	umts	-95	214	3	1140	10774738
P	2015-03-19 09:49:56	2015-03-19 09:51:06	70	23565	14615	umts	-95	214	3	1140	10774738
P	2015-03-19 09:49:56	2015-03-19 09:51:16	80	23565	14615	umts	-95	214	3	1140	10774738
P	2015-03-19 09:49:56	2015-03-19 09:51:26	90	23565	14615	umts	-95	214	3	1140	10774738
P	2015-03-19 09:49:56	2015-03-19 09:51:36	100	23565	14615	umts	-95	214	3	1140	10774738
P	2015-03-19 09:49:56	2015-03-19 09:51:46	110	23721	14735	umts	-95	214	3	1140	10774738
P	2015-03-19 09:49:56	2015-03-19 09:51:56	120	23721	14735	umts	-95	214	3	1140	10774738
F	2015-03-19 09:49:56	2015-03-19 09:52:06	130	23721	14848	umts	-95	214	3	1140	10774738
Once the connection has been fully disconnected, a new log will be written to syslog with the stats accumulated in the session:
mar 19 09:52:06 athena rmfd[12805]: Connection stats [from: 2015-03-19 09:49:56, to: 2015-03-19 09:52:06, duration: 130s] [rx: 23721, tx: 14848] [access tech: umts, rssi: -95dBm] [mcc: 214, mnc: 3, lac: 1140, cid: 10774738] [month 2015/3 rx: 23721, tx: 14848]
In addition to the last connection stats, the monthly accumulated RX/TX stats are also given.
If a connection is abruptly disconnected (e.g. system shuts down), the last valid record in the stats file is considered as the final record of the last connection, even if it's not a F (final) one. When rmfd restarts and detects that such situation happened, it will explicitly log to syslog the message corresponding to the last connection. In order to avoid additional logging to syslog of the same information it will also convert the last record to a F (final) one.
The stats log file is recreated every month. When rmfd detects that a new connection is happening in a month after the last one stored in the stats file, it will issue a new log to syslog before fully removing the stats log file contents:
mar 1 01:02:03 athena rmfd[999]: Month stats (2015/2) [rx: 586413, tx: 624682]
Assuming approximately 90 bytes per record, in the worst case of an ongoing connection 24/7 during the whole month, the size of the stats file may grow up to ~23MBytes:
90 * 6 * 60 * 24 * 31 = 24105600 ~23MB

# librmf
## Overview
The librmf library exposes the Modem C++ namespace, which includes the methods that allow remotely acting on the rmfd daemon. The user of the librmf library, doesn't need to know how the communication with the daemon is done.
All the methods implemented in the librmf library are synchronous and blocking. It is expected that if asynchronity is desired, the user application will take care of e.g. launching these methods in separate threads.
Errors in the librmf library methods will throw std::runtime_error exceptions, including a text string explaining the error that happened.
All the method executions in the librmf library are stateless and independent to each other. Multiple processes, or even multiple threads in the same process, can run actions in parallel using librmf.
By default the librmf library assumes that the communication with the rmfd daemon will be local through the standard UNIX socket. If the rmfd daemon is running in a different system and listening in a TCP port on a remote IP address, the client can instruct the library to default to using TCP/IP instead.
## Usage
The librmf library can be used by including the header file in the sources where you want to use the API methods:
#include <rmf-operations.h>
And also (assuming it was installed in /usr) adding the following arguments during the preprocessing and linking operations:
-I/usr/include/librmf	// preprocessing
-lrmf	// linking
A full simple example of usage is included later in section 4.4.
## API
The following sections show the application programming interface exposed by librmf.
### Library initialization API
bool SetTargetRemote (const std::string address,
        uint16_t port);
bool SetTargetLocal (void);
Before any other operation is done, the client can specify where the rmfd daemon is listening. By default the daemon is expected in the local UNIX socket, so this operation is only strictly needed if the daemon is listening on a remote (or local) TCP port.
The target setting may be changed only if there are no other API commands running.
### Device availability API
bool IsModemAvailable (void);
The user of the librmf library does not need to know which kind of modem is connected to the system, and not even which are the interfaces the modem is exposing. All that information is automatically managed by the rmfd daemon, which will just tell whether a suitable modem is available or not.
If more than one modem is available, or if a modem exposes multiple QMI interfaces, the first configured one will be used. If the modem is available but not ready to work (e.g. SIM card is missing), it will still be flagged as available, but the operations performed with it will end up failing.
### Device identification API
std::string GetManufacturer (void);
std::string GetModel (void);
std::string GetSoftwareRevision (void);
std::string GetHardwareRevision (void);
std::string GetImei (void);
The RaveModemFactory system allows to query the modem for several device identification strings, including the IMEI[14].
[14] http://en.wikipedia.org/wiki/International_Mobile_Station_Equipment_Identity
The device identification strings will be retrievable even if the SIM-PIN lock is enabled and locked.
### SIM identification API
struct PlmnInfo {
    uint16_t mcc;
    uint16_t mnc;
    bool gsm;
    bool umts;
    bool lte;
};

std::string GetImsi (void);
std::string GetIccid (void);
void GetSimInfo (uint16_t &operatorMcc,
        uint16_t &operatorMnc,
        std::vector<struct PlmnInfo> &plmns);
The RaveModemFactory system allows to query the modem for several SIM identification strings, including the IMSI[15] and the ICCID[16].
[15] http://en.wikipedia.org/wiki/International_mobile_subscriber_identity
[16] http://en.wikipedia.org/wiki/Subscriber_identity_module#ICCID
The GetSimInfo method returns not only the MCC/MNC[17] of the network operator which issued the SIM card (as per the EFad[18] SIM file), but also a list of other allowed operators with their access technologies (as per the EFoplmnwact[19] SIM file, if available).
[17] http://en.wikipedia.org/wiki/Mobile_country_code
[18] Administrative Data, 3GPP TS 31.121
[19] Operator Controlled PLMN Selector with Access Technology, 3GPP TS 31.121
Note that the previous methods may not return valid information until the SIM-PIN has been totally unlocked.
### SIM-PIN management API
bool IsSimLocked (void);
void Unlock (const std::string pin);
void EnablePin (bool enable,
        const std::string pin);
void ChangePin (const std::string pin,
        const std::string newPin);
In addition to checking the SIM-PIN status and unlocking it if necessary, the RaveModemFactory system also allows to enable, disable, and change the SIM-PIN lock code.
The IsSimLocked() method will return false if either the SIM-PIN is fully disabled or if it is enabled but already unlocked through Unlock().
Working with SIM-PUK is not directly available through the librmf interfaces. If for any reason the SIM gets locked asking for PUK, the qmicli tool can be used to unlock it using --dms-uim-unblock-pin.
### Dual SIM management API
uint8_t GetSimSlot (void);
void SetSimSlot (uint8_t slot);
The library allows controlling which is the currently used SIM for network registration and connection.
The GetSimSlot() method will return the index of the currently active SIM slot (1 or 2), and the SetSimSlot() method allows switching between both slots.
### Power management API
enum PowerStatus {
    Full,
    Low
};

PowerStatus GetPowerStatus (void);
void SetPowerStatus (PowerStatus powerStatus);
void PowerCycle (void);
The RaveModemFactory system allows to put the modem into low-power mode (i.e. RF off), and back to full-power mode (i.e. RF on). Obviously, the modem needs to be in full-power mode before it can be registered in the operator network.
If the modem is initially detected in low-power mode, the rmfd daemon will not automatically bring it into full-power mode. Additionally, re-setting the Full power status (even if it already is in that status) will trigger a new network scan if the modem is not yet registered to the operator network.
A full modem power cycle can also be requested using the PowerCycle() method. In this case, the rmfd daemon will reply as soon as the request has been accepted; i.e. it will not wait for the full reboot sequence to finish before replying.

### Network registration API
enum RegistrationStatus {
    Idle,
    Searching,
    Home,
    Roaming,
    Scanning
};

RegistrationStatus GetRegistrationStatus (std::string &operatorDescription,
        uint16_t &operatorMcc,
        uint16_t &operatorMnc,
        uint16_t &lac,
        uint32_t &cid);
void SetRegistrationTimeout (uint32_t timeout);
uint32_t GetRegistrationTimeout (void);
The RaveModemFactory has its own automatic logic to get registered in the mobile network. Therefore, librmf only allows checking the registration status, or querying and modifying the registration timeout before the built-in network scan request is launched.
The returned registration info includes not only the MCC/MNC[20] of the service provider network, but also the location area code[21] and cell id[22] where the modem is registered, which can be used to locate the position of the device with low accuracy.
[20] http://en.wikipedia.org/wiki/Mobile_country_code
[21] http://en.wikipedia.org/wiki/Mobility_management#Location_area
[22] http://en.wikipedia.org/wiki/Cell_ID
### Network status API
enum RadioInterface {
    Gsm,
    Umts,
    Lte
};
struct RadioPowerInfo {
    RadioInterface radioInterface;
    bool inTraffic;
    double txPower;
    bool rx0RadioTuned;
    double rx0Power;
    bool rx1RadioTuned;
    double rx1Power;
};

struct RadioSignalInfo {
    RadioInterface radioInterface;
    int32_t rssi;
    uint32_t quality;
};

std::vector<RadioPowerInfo> GetPowerInfo (void);
std::vector<RadioSignalInfo> GetSignalInfo (void);
The GetPowerInfo() method returns an array of structures which specify, per radio interface, whether the TX and RX chains are in traffic and what the power measurement is in each (given in dBm, only if in traffic).
 The GetSignalInfo() method returns an array of structures which specify, per radio interface, the quality of the network link. The quality is given both as the measured RSSI[23] (in dBm, where -125dBm or lower indicates no signal) and as a percentage.
[23] http://en.wikipedia.org/wiki/Received_signal_strength_indication
### Network connection API
enum ConnectionStatus {
    Disconnected,
    Disconnecting,
    Connecting,
    Connected
};

ConnectionStatus GetConnectionStatus (void)
void Connect (const std::string apn,
        const std::string user,
        const std::string password)
void Disconnect (void);
std:string GetDataPort (void);
The user of the librmf library can request connection to the network with the Connect() method, just passing the APN, user and password strings. If no user or password are needed, they should be given as empty strings.
The Connect() method will return only after all the connection steps have been performed, including the network interface and routing setup.
The Disconnect() method allows the user to request the disconnection from the network. In the same way, the method will only return once all the disconnection steps have been performed.
The Disconnecting and Connecting states returned by the GetConnectionStatus() method are only applicable when the method is run from another thread or process than the one which requested the actual connection or disconnection.
The GetDataPort() method will return the name of the network interface being managed by rmfd, useful for the case where multiple network interfaces are exposed by a single modem and only one is used.
### Network connection statistics API
bool GetConnectionStats (uint32_t &txPacketsOk,
        uint32_t &rxPacketsOk,
        uint32_t &txPacketsError,
        uint32_t &rxPacketsError,
        uint32_t &txPacketsOverflow,
        uint32_t &rxPacketsOverflow,
        uint64_t &txBytesOk,
        uint64_t &rxBytesOk);
The RaveModemFactory allows to query which are the number of received and transmitted packets and bytes in the ongoing connection, if any.
## Example
/*
 * Small librmf client example
 *
 * Assuming RMF was installed in /usr, compile with:
 * $> g++ -o example -I /usr/include/librmf -lrmf example.cpp
 */

#include <iostream>
#include <rmf-operations.h>

int
main (int argc, char **argv)
{
    std::string manufacturer;

    try {
        manufacturer = Modem::GetManufacturer ();
    } catch (std::exception const& e) {
        std::cout << "Exception: " << e.what() << std::endl;
        return -1;
    }

    std::cout << "Manufacturer: " << manufacturer << std::endl;
    return 0;
}
# rmfcli
The command line interface provided in the RaveModemFactory system allows to test every action that the librmf library exposes.
Note: rmfcli is just a test tool.
The suggested way to use RMF is to write a custom connection manager that uses librmf directly.

The tool can be run even if there is another user application using the librmf interfaces.
The following lines show the output of running rmfcli --help:
Usage: rmfcli <option>

Options:
-y, --target-address="ip"
-Y, --target-port="port"

Actions:
-f, --get-manufacturer
-d, --get-model
-j, --get-software-revision
-k, --get-hardware-revision
-e, --get-imei
-q, --get-sim-slot
-Q, --set-sim-slot="[1|2]"
-i, --get-imsi
-o, --get-iccid
-z, --get-sim-info
-L, --is-locked
-U, --unlock="pin"
-E, --enable-pin="pin"
-G, --disable-pin="pin"
-F, --change-pin="pin newpin"
-p, --get-power-status
-P, --set-power-status="[Full|Low]"
-Z, --power-cycle
-a, --get-power-info
-s, --get-signal-info
-r, --get-registration-status
-t, --get-registration-timeout
-T, --set-registration-timeout="timeout"
-c, --get-connection-status
-x, --get-connection-stats
-C, --connect="apn user password"
-D, --disconnect
-A, --is-available

Common actions:
-h, --help
-v, --version